## Slide 2: Introduction to Hydraulics
Gui Cavalcanti
4/17/2012

## Slide 3: Definition
Transmission of mechanical power via incompressible liquids
  Hydraulic Power = Flow X Pressure
  Pressure X Area = Force
  Flow / Area = Velocity
“Liquid gearing”

## Slide 4: Typical Hydraulic System
One centralized powerplant
Constant pressure (1,500 to 5,000 psi)
Variable (demand-based) flow rate
Flow-control or on/off valves controlling individual actuators

## Slide 5: Electric Motor Analogy
Imagine a DC electric motor system with the following attributes:
  Constant amperage
  Variable voltage
  Voltage-limited linear amplifiers
  Motors that never burned out
How would this system behave?

## Slide 6: Typical Hydraulic System

## Slide 7: System Attributes
“Force is free”
All movement is expensive
  Movement requires power (Flow X Pressure), regardless of physical load
Any actuator (subject to flow limitations) can produce up to full system power
Closed valves produce rigid actuators
Abrupt changes in valves produce abrupt mechanical movements

## Slide 8: Example Hydraulic Systems

## Slide 9: CAT 320D L

## Slide 10: CAT 320D L
CAT 320D L Medium-Class Excavator
52,000 lb operational weight
6,000 lb arm
46,000 lb drawbar pull
35 foot horizontal reach
25 foot digging depth
20,000+ lbf digging force

## Slide 11: CAT 320D L
How much power can the CAT 320D L Excavator’s engine generate?

## Slide 12: CAT 320D L

## Slide 13: CAT 320D L
148 horsepower

## Slide 14: Kia Spectra 2002
How much power can my crappy Kia Spectra’s engine generate?

## Slide 15: Kia Spectra 2002
126 horsepower

## Slide 16: Wait. What?

## Slide 17: Why?
Hydraulics offer perfect liquid gearing between the powerplant and actuators
Each joint’s performance is exactly bounded by cylinder size, cylinder placement, valve size, and system pressure
Raw power at low speeds = high forces

## Slide 18: Hydraulics
Engine
Pump

## Slide 19: Hydraulics
Hydraulics look “small”
  Fluid is incompressible; no big chambers are required for compression
  Limitations on size: material properties, bearing ratings
Trade size for heat generation

## Slide 20: Hydraulics Safety

## Slide 21: Hydraulics Safety
Hydraulic systems can harm you in multiple ways. They can easily:
  Burn you
  Cut off limbs
  Cause gangrene
  Cause blunt trauma

## Slide 22: Hydraulics Safety
Maintain a significant distance between you and any working hydraulic equipment
  Never service equipment while it’s running
Report any leaks immediately
Never leave a fitting partially tightened; either it’s on or it’s off all the way
Beware leaks in hoses
Assume parts can fly off at any time

## Slide 23: Requisite Terrifying Image

## Slide 24: Hydraulics Safety

## Slide 25: Hydraulic System Design

## Slide 26: Typical Hydraulic System

## Slide 27: Hydraulic System Design
A couple of standard components:
  Pump system
  Reservoir
  Accumulator
  Oil Cooler
  Filters
  Valves
  Actuators

## Slide 28: Pump System
Purpose:
  Provide fixed pressure (generally, 1,500 to 5,000 psi) constantly, and flow on demand
Solutions (in order of price, low to high):
  Create fluid flow constantly, but “dump” unused high pressure fluid (Industrial equipment)
  Create fluid flow as needed using human-controlled pumps (Lawn mowers, hydraulic tools)
  Create fluid flow as needed using mechanically-intelligent pumps (Airplanes, Boston Dynamics)

## Slide 29: Gear Pumps/Relief Valves
Fixed displacement pump
  Move X volume per revolution via interface between gear teeth and chamber wall
  Engine spinning at a given RPM produces a given flow rate
Relief valve opens at Y psi
  System builds up pressure to Y psi
  Any flow past the system demand flows through the bleed valve and into reservoir

## Slide 30: Reservoir
Purpose:
  Hold excess fluid
  Prevent turbulence
  Cool fluid
Two main types of circuits:
  Closed Circuit: No access to air. Reservoir is spring-loaded to a fixed low pressure.
  Open Circuit: Ready access to air. Reservoir is at atmospheric pressure.

## Slide 31: Accumulator
Purpose:
  Even out flow spikes on high pressure side due to actuator demands
Solutions:
  Embed a high-pressure gas bladder in a liquid tank
  Spring-load a plunger

## Slide 32: Oil Cooler
Purpose:
  Hydraulic systems are generally <50% efficient; everything else becomes heat

## Slide 33: Filters
Purpose:
  Keep particulates out of reservoir and pump
Particles as small as 10 microns can irretrievably damage a pump

## Slide 34: Valves
Purpose:
  Control fluid flow to actuators
Solutions:
  Solenoid valves (1 Hz; on/off)
  Proportional valves (10 Hz; tuned spring, current-controlled coils)
  Servo valves (100 Hz; small motors, tiny nozzles)

## Slide 35: Actuators
Purpose:
  Convert pressure and flow into force and velocity
Solutions:
  Cylinders
  Rotary motors
Extending Area
Retracting Area

## Slide 36: Questions?